## Slide 1: CFD Modeling of Reduced Lignin Black Liquor Combustion Markus Engblom, Niko DeMartini, Åbo Akademi
Soodakattilapäivä 30.01.2014

## Slide 2: Objective and CFD runs 1-3
CFD modeling for studying what operational changes may be needed when firing reduced lignin black liquor
CFD modeling of Wisaforest recovery boiler
  Run 1: Base Case, 100% MCR, flue gas O2 3% (wet)
  Runs 2 and 3: 10% and 20% lignin removed, total air adjusted for flue gas O2 3% (wet), other variables unchanged – presented here
  Runs 4-7: 10% & 20% lignin removed, modifications to air distribution and liquor spraying – spray modifications presented here, air cases to be run this fall

## Slide 3: Modeled Black Liquors (1/3)
 | Original Black Liquor (wt% d.s.) | Lignin [1] (wt% d.s.)
C | 32.2 | 64.5
H | 3.3 | 6
N | 0.09 | 0.1
Na | 21.4 | 0.3
K | 2.4 | 0.05
Cl | 0.3 | 0
Tot. S | 6.4 | 2.5
SO4 | 5.4 | 0
OH | 1.74 | 0
HHV (MJ/kg d.s.) | 13.2 | 26.5
Composition of reduced lignin BL
based:
Lignin content
of BL: 36 wt-%
175 kg H2SO4/ton
lignin precipitated [1]
1 Tomani, P. The lignoboost process. In Proceedings to The 2nd Nordic Wood Biorefinery Conf., 2-4 Sept. 2009,
Helsinki, Finland, pp. 181-188.

## Slide 4: Modeled Black Liquors (2/3)
 | Original Black Liquor (wt% d.s.) | 10% lower lignin (wt% d.s.) | 20% lower ligning (wt% d.s.)
C | 32.2 | 30.9 | 28.9
H | 3.3 | 3.2 | 3.03
N | 0.09 | 0.09 | 0.09
Na | 21.4 | 22.8 | 23.9
K | 2.4 | 2.6 | 2.7
Cl | 0.3 | 0.32 | 0.34
Tot. S | 6.4 | 7.0 | 7.5
SO4 | 5.4 | 6.7 | 7.87
OH | 1.74 | 1.4 | 1.1
HHV (MJ/kg d.s.) | 13.2 | 12.4 | 11.6

## Slide 5: Modeled Black Liquors (3/3)
 | Original Black Liquor | 10% lower lignin | 20% lower ligning
Liquor d.s. (wt-%) | 81.3 | 81.3 | 81.3
Volatiles (kg/kg d.s.) | 0.337 | 0.337 | 0.337
Char-C (kg/kg d.s.) | 0.143 | 0.103 | 0.074
Inorganics (kg/kg d.s.) | 0.516 | 0.555 | 0.585
Na2S (kg/kg d.s.) | 0.115 | 0.120 | 0.121
Na2SO4 (kg/kg d.s.) | 0.080 | 0.101 | 0.118
Na2CO3 (kg/kg d.s.) | 0.320 | 0.335 | 0.345
HHV (MJ/kg d.s.) | 13.2 | 12.4 | 11.6

## Slide 6: Liquor feed and combustion air
 | Original Black Liquor | 10% lower lignin | 20% lower ligning
Liquor feed (tds/d) | 5320 | 5160 | 5000
Of MCR (%) | 100 | 97 | 94
Air (kg/s) | 272 | 256 | 232
Air (Nm3/s) | 211 | 199 | 180
Primary | 23% | 23% | 23%
Secondary | 43% | 43% | 43%
Tertiary | 35% | 35% | 35%
Target flue gas O2 (% wet) | 3.0 | 3.0 | 3.0

## Slide 7: CFD calculation strategy
Set up Base Case
  Liquor and air mass flows
  Droplet size for C-balanced situation
Reduced ligning cases
  Liquor to 10% or 20% reduced lignin
  Total air for target 3% O2 (wet flue gas)
  Other variables remain the same

## Slide 8: ÅA CFD Recovery Furnace Model
Gas phase combustion
Droplet conversion
Char bed burning
Fluent based
ÅA sub-models for droplets and char bed

## Slide 9: Char bed burning model
Carbon accumulation
(g/s-m2)
Carbon input
by droplets
Char carbon
conversion

## Slide 10: CFD results

## Slide 11: Wisa liquor gun locations
Guns on left and right wall; 5 guns/wall

## Slide 12: Temperature
T (°C)
Original liquor
10% reduced lignin
20% reduced lignin
Side
view
Front
view

## Slide 13: O2 concentration
O2
(mole fraction)
Original liquor
10% reduced lignin
20% reduced lignin
Side
view
Front
view

## Slide 14: Carbon to walls/bed
(gC/s/m2)
Original liquor
10% reduced lignin
20% reduced lignin
Left wall, back wall, and char bed
≥

## Slide 15: Carbon to walls/bed
(gC/s/m2)
Original liquor
10% reduced lignin
20% reduced lignin
Right wall and front wall
≥

## Slide 16: Furnace char carbon loading
Chart: Carbon loading (kgC/s/m)
| 1.2792470011805901 | 0.37784731478452038 | 0.45082258512940149 | 0.56315305107719693 | 0.70391448176935345 | 0.47809987219015787 | 0.48809618786289055 | 0.4396581527191849 | 0.43312225100047835 | 0.39309133253552858 | 0.33682728587016242 | 0.28831515038205979 | 0.25277942532218439 | 0.27274712628857661 | 0.13439374134704815 | 6.9108377266287754E-2 | 4.7714369754332464E-2 | 1.7254328692100786E-2 | 6.3123335890608754E-3 | 2.1145840216744882E-3 | 6.0278538422732942E-4 | 2.1838899835200957E-4 | 5.8827985359084289E-5 | 1.934070751531544E-5 | 0 | 0 | 0 | 8.0586281313814099E-7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Base Case | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
10% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
20% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
low sec | 1.4 | 1.4
upper sec | 2.9 | 2.9
liquor | 6.7 | 6.7
low tert | 10.5 | 10.5
upper tert | 18.5 | 18.5
Base Case
-10% lignin
-20% lignin
Sec air
Tertair
Tertair
Liquor
Bullnose

## Slide 17: Furnace carbon char conversion
Chart: Carbon conversion (kgC/s/m)
| 2.4116495622146741 | 0.30878164824732901 | 0.31870610562452401 | 0.34664027734574582 | 0.38439364818418797 | 0.31247249993150172 | 0.3824652169182976 | 0.40638243862342416 | 0.42374684303242927 | 0.38940531305780868 | 0.3366991536828734 | 0.28787837273733891 | 0.25277942532218439 | 0.27264397568224447 | 0.13439374134704815 | 6.9108377266287754E-2 | 4.7714369754332471E-2 | 1.7254328692100786E-2 | 6.3123335890608763E-3 | 2.1145840216744882E-3 | 6.0278538422732942E-4 | 2.1838899835200957E-4 | 5.8827985359084289E-5 | 1.934070751531544E-5 | 0 | 0 | 0 | 8.0586281313814099E-7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Base Case | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
10% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
20% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
low sec | 1.4 | 1.4
upper sec | 2.9 | 2.9
liquor | 6.7 | 6.7
low tert | 10.5 | 10.5
upper tert | 18.5 | 18.5
Base Case
-10% lignin
-20% lignin
Sec air
Tertair
Tertair
Liquor
Bullnose

## Slide 18: Fate of char carbon
(kg/s) | Base Case | 10% reduced lignin | 20% reduced lignin
In liquor feed | 8.81 | 6.19 | 4.30
in-flight conversion | 3.90 | 2.60 | 1.79
to bed/walls | 4.91 | 3.59 | 2.51
conversion on bed/walls | 4.70 | 4.37 | 4.10
carbon accumulation | 0.21 | -0.78 | -1.59

## Slide 19: Fate of char carbon
(%) | Base Case | 10% reduced lignin | 20% reduced lignin
In liquor feed | 100.0 | 100.0 | 100.0
in-flight conversion | 44.3 | 42.0 | 41.6
to bed/walls | 55.7 | 58.0 | 58.4
conversion on bed/walls | 53.4 | 70.5 | 95.5
carbon accumulation | 2.3 | -12.5 | -37.1

## Slide 20: Carbon accumulation and comb. air
 | Base Case | 10% reduced lignin | 20% reduced lignin
carbon accumulation (kg/s) | 0.21 | -0.78 | -1.59
Air to balance carbon (kg/s) | 2.4 | -8.9 | -18.2

## Slide 21: Conclusions - Runs 1-3
Less char-C with lignin removal
Lower furnace less loaded with char-C
Dynamic situation of more carbon conversion than delivery
Operational changes
  Reduce prim/sec air (runs 4 & 5) and/or
  Change spraying – larger droplets (runs 6 & 7)

## Slide 22: Runs 4 & 5 – Reduced air
Primary and secondary air need to be reduced to reflect the reduced char carbon load to the lower furnace
Not presented here - to be run this fall

## Slide 23: Runs 6 & 7 – Larger Droplets
Larger droplets will result in more carbon reaching the lower furnace - to provide a carbon balance based on the original primary, secondary and tertiary air distribution
In practice this larger particle size distribution would be achieved by reducing the firing temperature or changing the spray angle or nozzle

## Slide 24: CFD runs 6 and 7
Objective:
  Increase char-carbon delivery to lower furnace until carbon accumulation ≈ 0
  By increasing droplet size in liquor spray (lower liquor T)
  Spray angle and nozzle unchanged
Run 6: 10% lignin removed
Run 7: 20% lignin removed

## Slide 25: CFD runs 6 and 7
Note: Droplet size, liquor temperature, droplet velocity, etc – freely adjustable, independent parameters in CFD model
For Runs 6 and 7, droplet size, droplet velocity, and liquor temperature linked to each other in CFD model
How are droplet size and droplet velocity connected to liquor temperature?

## Slide 26: Spray characterization (Miikkulainen et al.)
Nozzle A
Nozzle B
 | Nozzle A | Nozzle B
Nozzle pipe diameter | 27 mm | 28 mm
Splash plate angle | 23° | 36°
Nozzle exit area reduced by plate? | Partly reduced | Not reduced

## Slide 27: Liquor T - droplet size – dependence
Nozzle A
Nozzle B

## Slide 28: Liquor T - droplet size – dependence
Generic correlation for CFD
Dp(mm) = -1.46·T(°C)+32.5

## Slide 29: Liquor T - droplet size – dependence
Nozzle A
Nozzle B
Correlation
Correlation

## Slide 30: Liquor T - droplet velocity – dependence
Nozzle A
Dimensionless velocity, v(-)
v(-) =
Actual Liquor Velocity
Liquor Velocity assuming
no flashing

## Slide 31: Liquor T - droplet velocity – dependence
Nozzle A
10% and 20% reduced lignin
Cases, liquor mass flow ~7 kg/s

## Slide 32: Liquor T - droplet velocity – dependence
Nozzle A
Nozzle B
10% and 20% reduced ligning
Cases, liquor mass flow ~7 kg/s

## Slide 33: Liquor T - droplet velocity – dependence
v(-) = 0.057·T(°C)+0.668
Generic correlation for CFD

## Slide 34: Liquor T - droplet velocity – dependence
Nozzle A
Nozzle B
Exp
Exp
Correlation
Correlation

## Slide 35: CFD runs 6 and 7 vs. Base Case
 | Base Case | 10% reduced lignin (Run 6) | 20% reduced lignin (Run 7)
Average droplet size | 5.7 mm | 12.5 mm | 23.0 mm
Initial droplet velocity | 15.0 m/s | 12.7 m/s | 9.2 m/s
Excess temperature | 18.4 °C | 13.7 °C | 6.5 °C
Liquor T changed from Base Case |  | -4.7 °C | -11.9 °C

## Slide 36: Temperature (-10% lignin)
T (°C)
10% reduced lignin with dp 5.7 mm
Side
view
Front
view
10% reduced lignin with dp 12.5 mm

## Slide 37: Temperature (-20% lignin)
T (°C)
20% reduced lignin with dp 5.7 mm
Side
view
Front
view
20% reduced lignin with dp 23.0 mm

## Slide 38: Carbon to walls/bed (-10% lignin)
(gC/s/m2)
Original liquor
10% reduced lignin with dp 5.7 mm
Left wall, back wall, and char bed
≥
10% reduced lignin with dp 12.5 mm

## Slide 39: Carbon to walls/bed (-10% lignin)
(gC/s/m2)
Original liquor
Right wall and front wall
≥
10% reduced lignin with dp 5.7 mm
10% reduced lignin with dp 12.5 mm

## Slide 40: Carbon to walls/bed (-20% lignin)
(gC/s/m2)
Original liquor
Left wall, back wall, and char bed
≥
20% reduced lignin with dp 5.7 mm
20% reduced lignin with dp 23.0 mm

## Slide 41: Carbon to walls/bed (-20% lignin)
(gC/s/m2)
Original liquor
Right wall and front wall
≥
20% reduced lignin with dp 5.7 mm
20% reduced lignin with dp 23.0 mm

## Slide 42: Furnace carbon loading (-10%)
Chart: Carbon loading (kgC/s/m)
| 1.2792470011805901 | 0.37784731478452038 | 0.45082258512940149 | 0.56315305107719693 | 0.70391448176935345 | 0.47809987219015787 | 0.48809618786289055 | 0.4396581527191849 | 0.43312225100047835 | 0.39309133253552858 | 0.33682728587016242 | 0.28831515038205979 | 0.25277942532218439 | 0.27274712628857661 | 0.13439374134704815 | 6.9108377266287754E-2 | 4.7714369754332464E-2 | 1.7254328692100786E-2 | 6.3123335890608754E-3 | 2.1145840216744882E-3 | 6.0278538422732942E-4 | 2.1838899835200957E-4 | 5.8827985359084289E-5 | 1.934070751531544E-5 | 0 | 0 | 0 | 8.0586281313814099E-7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Base Case | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
10% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
10% reduced lignin, dp 12.5mm | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027 | 61.4436
low sec | 1.4 | 1.4
upper sec | 2.9 | 2.9
liquor | 6.7 | 6.7
low tert | 10.5 | 10.5
upper tert | 18.5 | 18.5
Base Case
-10% lignin
-10% lignin, dp 12.5 mm
Sec air
Tertair
Tertair
Liquor
Bullnose

## Slide 43: Furnace carbon conversion (-10%)
Chart: Carbon conversion (kgC/s/m)
| 2.4116495622146741 | 0.30878164824732901 | 0.31870610562452401 | 0.34664027734574582 | 0.38439364818418797 | 0.31247249993150172 | 0.3824652169182976 | 0.40638243862342416 | 0.42374684303242927 | 0.38940531305780868 | 0.3366991536828734 | 0.28787837273733891 | 0.25277942532218439 | 0.27264397568224447 | 0.13439374134704815 | 6.9108377266287754E-2 | 4.7714369754332471E-2 | 1.7254328692100786E-2 | 6.3123335890608763E-3 | 2.1145840216744882E-3 | 6.0278538422732942E-4 | 2.1838899835200957E-4 | 5.8827985359084289E-5 | 1.934070751531544E-5 | 0 | 0 | 0 | 8.0586281313814099E-7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Base Case | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
10% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
10% reduced lignin, dp 12.5 mm | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027 | 61.4436
low sec | 1.4 | 1.4
upper sec | 2.9 | 2.9
liquor | 6.7 | 6.7
low tert | 10.5 | 10.5
upper tert | 18.5 | 18.5
Base Case
-10% lignin
-10% lignin, dp 12.5 mm
Sec air
Tertair
Tertair
Liquor
Bullnose

## Slide 44: Furnace carbon loading (-20%)
Chart: Carbon loading (kgC/s/m)
| 1.2792470011805901 | 0.37784731478452038 | 0.45082258512940149 | 0.56315305107719693 | 0.70391448176935345 | 0.47809987219015787 | 0.48809618786289055 | 0.4396581527191849 | 0.43312225100047835 | 0.39309133253552858 | 0.33682728587016242 | 0.28831515038205979 | 0.25277942532218439 | 0.27274712628857661 | 0.13439374134704815 | 6.9108377266287754E-2 | 4.7714369754332464E-2 | 1.7254328692100786E-2 | 6.3123335890608754E-3 | 2.1145840216744882E-3 | 6.0278538422732942E-4 | 2.1838899835200957E-4 | 5.8827985359084289E-5 | 1.934070751531544E-5 | 0 | 0 | 0 | 8.0586281313814099E-7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Base Case | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
20% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027 | 61.4436
20% reduced lignin, dp 23.0mm | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027 | 61.4436
low sec | 1.4 | 1.4
upper sec | 2.9 | 2.9
liquor | 6.7 | 6.7
low tert | 10.5 | 10.5
upper tert | 18.5 | 18.5
Base Case
-20% lignin
-20% lignin, dp 23.0 mm
Sec air
Tertair
Tertair
Liquor
Bullnose

## Slide 45: Furnace carbon conversion (-20%)
Chart: Carbon conversion (kgC/s/m)
| 2.4116495622146741 | 0.30878164824732901 | 0.31870610562452401 | 0.34664027734574582 | 0.38439364818418797 | 0.31247249993150172 | 0.3824652169182976 | 0.40638243862342416 | 0.42374684303242927 | 0.38940531305780868 | 0.3366991536828734 | 0.28787837273733891 | 0.25277942532218439 | 0.27264397568224447 | 0.13439374134704815 | 6.9108377266287754E-2 | 4.7714369754332471E-2 | 1.7254328692100786E-2 | 6.3123335890608763E-3 | 2.1145840216744882E-3 | 6.0278538422732942E-4 | 2.1838899835200957E-4 | 5.8827985359084289E-5 | 1.934070751531544E-5 | 0 | 0 | 0 | 8.0586281313814099E-7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Base Case | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027
20% reduced lignin | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027 | 61.4436
20% reduced lignin, dp 23.0 mm | 0.6392 | 1.8801 | 3.121 | 4.3619 | 5.6028 | 6.8437 | 8.0846 | 9.3255 | 10.5664 | 11.8074 | 13.0483 | 14.2892 | 15.5301 | 16.771 | 18.0119 | 19.2528 | 20.4937 | 21.7346 | 22.9755 | 24.2164 | 25.4573 | 26.6982 | 27.9391 | 29.18 | 30.4209 | 31.6618 | 32.9027 | 34.1436 | 35.3846 | 36.6255 | 37.8664 | 39.1073 | 40.3482 | 41.5891 | 42.83 | 44.0709 | 45.3118 | 46.5527 | 47.7936 | 49.0345 | 50.2754 | 51.5163 | 52.7572 | 53.9981 | 55.239 | 56.4799 | 57.7209 | 58.9618 | 60.2027 | 61.4436
low sec | 1.4 | 1.4
upper sec | 2.9 | 2.9
liquor | 6.7 | 6.7
low tert | 10.5 | 10.5
upper tert | 18.5 | 18.5
Base Case
-20% lignin
-20% lignin, dp 23.0 mm
Sec air
Tertair
Tertair
Liquor
Bullnose

## Slide 46: Fate of char carbon (-10%)
(kg/s) | Base Case | 10% reduced lignin, dp 5.7 mm | 10% reduced lignin, dp 12.5 mm
In liquor feed | 8.81 | 6.19 | 6.19
in-flight conversion | 3.90 | 2.60 | 1.01
to bed/walls | 4.91 | 3.59 | 5.18
conversion on bed/walls | 4.70 | 4.37 | 5.16
carbon accumulation | 0.21 | -0.78 | 0.02

## Slide 47: Fate of char carbon (-20%)
(kg/s) | Base Case | 20% reduced lignin, dp 5.7 mm | 20% reduced lignin, dp 23.0 mm
In liquor feed | 8.81 | 4.30 | 4.30
in-flight conversion | 3.90 | 1.79 | 0.24
to bed/walls | 4.91 | 2.51 | 4.05
conversion on bed/walls | 4.70 | 4.10 | 4.02
carbon accumulation | 0.21 | -1.59 | 0.03

## Slide 48: Fate of char carbon (-10%)
(%) | Base Case | 10% reduced lignin, dp 5.7 mm | 10% reduced lignin, dp 12.5 mm
In liquor feed | 100.0 | 100.0 | 100.0
in-flight conversion | 44.3 | 42.0 | 16.3
to bed/walls | 55.7 | 58.0 | 83.7
conversion on bed/walls | 53.4 | 70.5 | 83.4
carbon accumulation | 2.3 | -12.5 | 0.3

## Slide 49: Fate of char carbon (-20%)
(%) | Base Case | 20% reduced lignin, dp 5.7 mm | 20% reduced lignin, dp 23.0 mm
In liquor feed | 100.0 | 100.0 | 100.0
in-flight conversion | 44.3 | 41.6 | 5.7
to bed/walls | 55.7 | 58.4 | 94.3
conversion on bed/walls | 53.4 | 95.5 | 93.6
carbon accumulation | 2.3 | -37.1 | 0.7

## Slide 50: Conclusions - Runs 6 and 7
With lignin removal and air split unchanged considerably larger droplets are needed to reach carbon balanced situation (=”steady operation”)
Estimated to correspond to a decrease in liquor temperature of 4.7 °C or 11.9 °C when 10% or 20% lignin removed respectively
Results suggest both liquor temperature and air distribution will need to be adjusted

## Slide 51: Recommended Air Distribution – Runs 4 & 5
 | Run 4 | Run 5
Lignin Removed | 10% | 20%
Total Air (kg/s) | 256 | 232
Primary (kg/s) | 50 | 35
Secondary (kg/s) | 110 | 100
Tertiary (kg/s) | 96 | 97
Primary (%) | 20 | 15
Secondary (%) | 43 | 43
Tertiary (%) | 37 | 42